Operating Systems CS 370

I/O System

Text:

Operating Systems Concepts with Java, 8th Ed., Silberschatz, Galvin, & Gagne

Chapter 13-13.4

Objectives:

During this class the student shall learn to:

Relate how interrupts affect processing in an operating system

Define interrupt vector, device driver, interrupt handler, device controller.

Contrast the efficiency of polling, interrupts, and DMA.

Describe the 9 steps a processor takes to process interrupts (i.e., memorize).

Time Allocation:

Class time will be allocated as follows:

I/O & Interrupts				1 hour

TOTAL: 					1 hours

### I/O Structure

Devices include:

Storage devices: disk, floppy disk

Communications devices: keyboard, display, serial port

Two types of devices:

Block-oriented: Transfers occur a block at a time (block = N bytes)

- E.g. disks, tapes.

Stream-oriented: Transfers occur one byte at a time.  Includes:

- line-at-a-time:  Processed only when End of Line is received

E.g. terminal, network communications port

- byte-at-a-time:  Each keystroke is significant.

E.g. mouse, sensors.

Computer-Device Interface

Components of a Computer

Application Programming Interface (API): Common application interface

Device Driver: S/W in O.S. memory gives orders to the device controller

Interrupt Vector:  Array of pointers to interrupt routines, indexed by interrupting device.

In lower addresses of memory

Bus Interface: How Computer processor communicates with device

Components of Device

Device Controller: Intelligence that drives device & communicates with CPU.

Device (H/W)

Device Driver: Logic to control an external device.

Includes logic to initialize device

Initiates transmit or receive operation by placing command in command register of device controller

Includes interrupt handler: Processes the interrupt when the operation is complete.

Reconfigurable Device Drivers

- Device & driver from third party (not OS distributer)

- Eliminates the need to recompile O.S. for each new driver

- Open Systems allow plug-in device drivers

  - Defined API

  - Allows device driver to allocate buffer space & manipulate kernel tables.

Device Controller: The intelligent part of device which interfaces with the computer

Controller sets Status bits to indicate the status of the last requested operation:

Busy: Device is still executing the command

Done: Operation is completed

Error: Error code if operation failed

Performing I/O

Example: The device driver has a number of characters to send to a terminal.

To Begin Transmission:

The device driver requests a UART (Universal Asynchronous Receiver Transmitter) to transmit a byte. At 9600 bits per second, the byte will finish transmitting in 1 ms (0.00104 second).

While the byte is transmitting the processor can wait OR the processor can do other work.

Three methods of receiving status from Device Controller:

- If polling is used the device driver will busy-wait (test repeatedly) to see if the UART is done.

- If interrupts are used the processor performs other work until the UART indicates (via interrupt) that the operation (transmit byte) is complete.

- If DMA is used the DMA controller sends the entire packet and interrupts when packet is sent.

When the processor determines that the byte is transmitted (or received) the device driver performs an I/O command to transfer (or receive) the next byte.

Bytes are received/sent from a buffer, which must remain in memory.

When buffer is empty, the interrupt must schedule a process to initialize new buffer for transmit/receive and reissue communications command.

Types of Interrupts

High Priority:  Cannot be inhibited

Hardware Failure: E.g. Memory parity error or power failure

Program:

Arithmetic overflow

Divide by zero

Execute illegal instruction

Lower Priority: Inhibitable

Timer: Interrupts the processor every n time units.

I/O: Signals completion of an operation or an error condition.

Software Trap:  Command in system call interface changes mode from user to kernel mode

Definitions:

Steps by device driver to initiate an I/O operation include:

- Wait for I/O device to become free

- Prepare to request an I/O device to do an operation: Set up registers, buffers.

- Perform the I/O command to initiate the operation.

- When the external device is completed, the device interrupts the processor.

Interrupt Processing includes:

- Device controller issues an interrupt signal to the processor.

- Processor finishes execution of current instruction before checking for interrupt.

- Processor sends an acknowledgment signal to the device that issued the interrupt.

- Processor saves info on currently executing process (e.g. address of next instruction) on stack.

- Processor jumps to interrupt handler.

- Interrupt handler saves off all registers (it will be using) onto stack.

- Interrupt handler handles the interrupt: e.g. put received data in a buffer or get next byte from buffer to send; may start another I/O operation.

- Interrupt handler restores registers that were modified from stack.

- Restore registers from stack and return to interrupted program.

### Draw:

Multiprogramming, Multiprocessing, Cluster:

#### Interrupts:

Show the nine steps of processing an interrupt on the following graph.  Assume input was entered from the keyboard.

# Text boxes

CPU - ALU

Cache

Disc

Controller

USB Cntrlr

Display

Controller

LAN

Controller

Memory-I/O Bus

Memory

CPU - ALU

Cache

Disc

Controller

USB Cntrlr

Display

Controller

LAN

Controller

Memory-I/O Bus

Memory