Introduction

Operating Systems CS 370

Text:

Chapters 1, 2-2.5 (Optional 2.7)

Operating Systems Concepts with Java, 8th Ed., Silberschatz, Galvin, & Gagne

Objectives:

During this class the student shall learn to:

Define terms used in Operating Systems:

Define terms: batch, real-time system, multiprogramming, LAN, MAN, WAN, work station, multiprocessor, asymmetric multiprocessor, symmetric multiprocessor, core, fault tolerant, blade server, cluster, virtual machine, network operating system, shell, timesharing.

Define and describe: kernel mode, user mode.

Describe and draw a graph showing the difference between multiprogramming, multiprocessors and a distributed system.

Describe the different levels and functions of memory used in an OS: primary, secondary, tertiary.

Define volatile and describe which memory devices are volatile.

Analyze how an OS initiates and terminates processes using fork().

Describe the purpose of the System Call Interface

List example calls from the major OS subsystems.

Time Allocation:

Class time will be allocated as follows:

Course & O.S. Introduction 			½ hour

O.S. Vocabulary 				1.0 hour

Memory Subsystems				½ hour

System Call Interface				½ hour

Fork Lab & Process Intro			1 hour

TOTAL: 					4 hours

Operating Systems

Computer system can be divided into 3 components:

- hardware (H/W)

- operating system (O.S.)

- system and applications programs

Systems Software: Provides a general programming environment for applications: compilers, linkers, network protocols, text editors, debuggers, etc.

Goals:

convenient to the user

efficient

Operating System: resource allocator

CPU time

memory space

file storage space

I/O devices

Concerned with resource sharing and resource isolation

O.S. History

Early Computers

Late 40s to mid 50s

Serial Processing: One user had access to the computer at a time.

Program loaded in by hand or by card reader

Programmer used LEDs (lights) and toggle switches to look at registers, step through instructions, halt processor, ...

Early Systems

Bootstrap Program: ROM contains logic to load OS from disk or tape.

Batch:  Jobs are queued or ‘spooled’ waiting to be processed.

Examples of Batch Processing:

JCL: IBM's Job Control Language

UNIX Shell Command File:  List of commands are executed from a file

Shell: Command interpreter processes each command (in file or at command prompt).

Includes programming language constructs.

Multiprogramming

Reading in one program, executing another, sending output for a third...

Why?  Computers got faster but I/O did not speed up at same rate.

I/O operations left processor idle.

Solution: Run another program while reading in a new program.

Must expand memory to support multiple jobs.

Features introduced on Monitor-type computer operating systems:

Multiprogramming: Support >= 3 programs concurrently.

Memory protection: Application programs cannot alter Monitor private data.

Timer: Application programs allowed to run for a specified amount of time.

Interrupts: Gives monitor control over application program.

Privileged instructions: The monitor only can execute I/O instructions, inhibit interrupt instructions...

If application attempts to do a privileged instruction, a hardware interrupt occurs and monitor resumes.

Supervisory or kernel mode: A mode bit determines when all instructions are allowed.

User mode: An application mode with limited instructions

Time Sharing

Multiple users share costly computers.

Features emphasized:

Response time, resource management & protection

Multiple processes in memory, multiprogramming.

Examples: UNIX, Linux

PC: Personal Computer & Work Stations

Hardware costs decreased: Processor is single integrated circuit

Computer system dedicated to a single user: Predictable response times

Initially simplified O.S (MS DOS): lack of security, multitasking functions

Work Station: Has more memory, faster processor, high resolution graphics, networked.

Server:

Networked System

Multiple processors connect with each other via communications links.

Local Area Network (LAN): Single 10-1000 Mbps cable connects many computers locally (room/floor/building)

Metropolitan Area Network (MAN): Network spans buildings, campus, city.

Wide Area Network (WAN):  Links buildings, cities, countries.

Network includes: specialized servers: disk/file/database, printer, communications

Client/server: Clients (user machines) request services from servers.

Advantages:

Reliability: if one processor fails, another can take over.

Resource Sharing: Share printer, plotter, disks

Computational Speedup: Application execution can be spread over multiple processors.

Communication: E.g. email

Networked Operating System: A collection of networked computers that share a file system and can send messages between processes.

Parallel Processors / Multiprocessors

Multiprocessor: Multiple processors share a bus, memory, clock, I/O devices.

Multicore:  A chip with multiple processors

Parallel Processing: Multiple processors used to speed up execution of a single program.

Advantages:

Reliability: if one processor fails, another can take over.

Throughput: application execution can be spread over multiple processors

Economy of Scale:  shared resources: storage, peripherals, power.

Asymmetric Multiprocessing:  A master processor gives orders to slaves

Symmetric Multiprocessing: Multiprocessors are peers; all share OS structures

Blade Servers: Processor, I/O, Network boards each have own OS and operate independently in the same chassis.

Cluster: Computer systems networked (via LAN) to provide high availability.

Fault Tolerant:  System continues operation in spite of any single component failure

Storage Area Network (SAN): Many computer systems attach to a pool of storage

Real-Time Systems

When processing completes is as important as how correct the processing is.

Applications: industrial control, robotics, weapons systems, medical imaging, telephony.

Virtual Machine (VM)

A system supports multiple operating systems simultaneously.

Each process is only aware of the single operating system it is working with.

A VM implementation allows each kernel to think they are interfacing to the actual computer hardware

Actually the VM implementation intercedes in all accesses to hardware

Each kernel operates in user mode on the base machine

Each VM has own minidisk or share a disk

Timer issues occur

Advantages: Running non-native software; testing operating systems.

#### Example VM: Java Virtual Machine

Interpret one bytecode at a time OR

Just-in-time compiler: converts bytecodes into machine language of host computer OR

Execute bytecodes natively

Question: What is the difference between multiprogramming, multiprocessing, and distributed systems?

# Computer System & OS Structures

A computer system generally has:

CPU

Bus: Enables CPU to communicate with:

Disk Controller  & Disk

Printer Controller & Printer

Memory Controller & Memory

Operating System components include:

Process Management

Main-Memory Management

File Management

I/O System Management

Secondary-Storage Management

Networking

Protection System

Command-Interpreter System

We review each in turn.

## Process Management

A process is approximately a program in execution.

However processes can spawn child processes in UNIX via a fork() call:

cout << “Ha “ << endl;	// one process

fork();

cout << “He “ << endl;	// two processes

fork();

cout << “Ho “ << endl;	// four processes

OS Functions include:

Create/Delete user & system processes

Process synchronization and communication

## Memory Management

But Memory can consist of many different devices.

Memory Management consists of Main-Memory Management, Secondary-Storage Management and File Management

### Introduction to Memory Hierarchy

Why multiple types of memory are necessary:

- Processor speed is constrained by memory speed to access instructions, data.

- Faster memory costs more than slower memory.

- Principle of Locality: Accesses tend to cluster:

Do loops and functions repeat the same code and data accesses.

Instructions execute mostly sequentially.

Levels of Memory:  Fast->slow includes:

Registers: Volatile memory

Cache: Volatile memory

Primary or Main Memory:  Temporary storage for processing

Secondary Memory: Magnetic Disk / Electronic Disk:  Hold large quantities of available data

Tertiary Memory: Magnetic Tape / Optical Disk: Backup or archival storage

Cheap but fast implementation includes:

Small amount of very high-speed memory.

Larger amount of high-speed memory.

Huge quantities of low-speed memory

Main Memory:  Dynamic Random Access Memory (DRAM)

Volatile storage: Loss of contents upon power loss.

Magnetic Disks

Nonvolatile storage: Retains memory after loss of power.

Access: Seek time, Rotational delay, Transfer time.

### Main-Memory Management

OS Functions include:

Process isolation: A program cannot modify another program's data.

Automatic Allocation / Mgmt: Memory allocated according to memory hierarchy transparent to programmer.

Modular Programming Support: Program can dynamically allocate / deallocate memory.

Protection & Access Control: Allow sharing of data when permissions permit (e.g. files).

Long-term Storage: Storage of info for extended periods.

Virtual memory: Allows programs to address memory from a logical point of view w/o regard to amount of main memory physically available.

Allows an executing program to have only a portion of program / data in memory.

Maps a program's virtual addresses into a physical address.

Accesses and manages data in cache, main memory, disk as necessary.

### Secondary Storage Management

OS Functions include:

Free-space management: Tracks unused portion of disk

Storage allocation: Tracks allocation of blocks to files

Disk scheduling: Schedules disk writes and reads

### File System Management

Primary operations include:

Open: Prepares file for reading, writing

Read

Write

Close: Releases locks & system resources

Seek: Set file pointer to specific location

OS Functions include:

Creating / Deleting files and directories

Supporting operations for manipulating files and directories

Mapping files onto secondary storage

Backing up files on stable storage media

## I/O Management

Goal: Hide details of specific hardware devices from the user.

OS Functions include:

A memory-management function that performs buffering, caching, and spooling

A general device-driver interface

Hardware-specific drivers

## Protection System

Security: Protect one user or group from another’s activities

Protection of files, memory, CPU, other resources

Detection of & protection against malicious, unauthorized or incompetent user

## Command-Interpreter System

System Call Interface:  Interface between user and operating system.

Can be part of or external to kernel

CUI: Command User Interface

Shell: Unix command line interpreter

GUI: Graphical User Interface

Uses desktop, mouse, folders, and icons to execute commands

## Networking

Communications network connects processors in a system

Uses Communications Protocol to interface with other computer systems

## System Calls

Provides a controlled interface between an application and the operating system.

Controlled interface must ensure operating system cannot be corrupted (by verifying all system call parameters)

Defines the Application Programming Interface (API)

Transfers control from User mode to Kernel Mode

(From Figure 3.2 of Applied Operating Systems Concepts)

Process control

End, abort

Load, execute

Create process, terminate process

Get process attributes, set process attributes

Wait for time

Wait event, signal event

Allocate, free memory

File management

Create / delete file

Open, close

Read, write, reposition/seek

Get / Set file attributes

Device Management

Request / Release device

Read, write, reposition

Get / Set device attributes

Attach / Detach devices

Information maintenance

Get / Set time or date

Get / Set system data

Get / Set process, file or device attributes

Communications

Create / Delete communication connection

Send, receive messages

Transfer status information

Attach / Detach remote devices

### Lab on Processes:

###### Intro:

The purpose of this lab is to analyze how an OS initiates and terminates processes using fork(), and how the OS intersperses output from different processes.

###### Method:

Enter the following two files and execute in the lab:

Program1.cpp					Program2.cpp

#include <iostream>				#include <iostream>

#include <unistd.h>				#include <unistd.h>

using namespace std;				using namespace std;

int main()					int main()

{						{

cout << “Ha! “ << endl;			cout << “Ha! “;

fork();						fork();

cout << “Ho! ” << endl;			cout << “Ho! “;

fork();						fork();

cout << “He! “ << endl;			cout << “He! “ << endl;

}						}

Compile and run as follows:

$ g++ simplefork.cpp –o simplefork

$ ./simplefork

#### Results:

List the output for both programs below.

#### Analysis:

Why are we seeing what we are seeing?  What is the operating system doing?

###### Conclusion:

What did you learn from this?

### Define System Calls

List specific C/C++ or Java function calls that must include a system call.

Process Control

File Manipulation

Device manipulation

Information maintenance

Communications