Operating Systems CS 370

CPU Scheduling

Text:

Chapter 5

Operating Systems Concepts with Java, 7th Ed., Silberschatz, Galvin, Gagne

Objectives:

During this class, the student shall be able to:

Define I/O-bound, CPU-bound and race condition.

Define the functions of the short-term, long-term scheduler.

Describe the difference between preemptive and nonpreemptive schedulers.

Define and be able to calculate: CPU utilization, throughput, wait time, response time, and turnaround time.

Be able to calculate the order and timing of processes through the CPU using the following algorithms: FCFS, RR, Priority, Shortest Job First, Shortest Remaining Time, Multilevel Feedback Queue.

Define the difference between SMP and asymmetric multiprocessing as it relates to operating systems.

Define processor affinity and load balancing, and why each is important.

Time Allocation:

Class time will be allocated as follows:

Intro						1/2 hour

Scheduling Criteria				1/2 hour

Scheduling Algorithms			2 hours

TOTAL:					3 hours

CPU Scheduling

Introduction

Program execution is characterized by alternating sequences of:

CPU burst

I/O burst

Two types of programs:

I/O-bound: short CPU bursts

CPU-bound: long CPU bursts.

Goal: Balancing I/O-bound and CPU-bound jobs.

CPU Scheduler

Long Term Scheduling: Decides when to add to the pool of processes to be executed.

Controls degree of multiprogramming.

When a job terminates, scheduler may decide to add one or more jobs.

Batch jobs: Spooled on disk until ready to process

Interactive: User logs in O.S. must accept new process.

Medium Term Scheduling: Decides when to add to the number of processes that are partially or fully in main memory.

Who wins memory?

Global scope memory allocation impacts decision.

Short Term Scheduler: Decides which available process will be executed next by the processor.

Short Term Scheduler:

When CPU becomes idle, OS selects a process in ready queue to be executed.

The Ready queue holds PCBs.

Short Term Scheduling functions include:

Enqueuer function: Adds PCB to appropriate Ready Queue (possibly after deciding priority).

Dispatcher function: Selects process for execution and passes control to it.  Includes:

Switches context

Switches to user mode

Jumps to proper location in user program.

CPU reschedules processes:

- When context switches from running state to blocked state (e.g. I/O request) or yields CPU.

- When process terminates.

- When context switches from running state to ready state (e.g. timer interrupt)

- When context switches from blocked state to ready state (e.g. I/O completion)

Two types of scheduling:

Nonpreemptive:  Scheduling only takes place during 1 & 2 above.

The process retains the CPU until it releases the CPU by terminating or by blocking.

Used by Microsoft Windows 3.X

Preemptive:  Scheduling may take place during all four event types.

Can preempt on: clock or I/O interrupt, OS call, signal.

Advantage: Prevents any process from monopolizing the processor.

Disadvantage: More overhead due to context switching.

Used by Microsoft Windows 95 and later, UNIX.

Race Condition Problem: If two processes share data, one may be in midst of updating the data when it is preempted and second process is run

Problem: Single processor, preemptive OS

Problem: Multiprocessor, preemptive or non-preemptive OS

Solution: Semaphores

Scheduling Criteria

Statistics to measure successfulness of CPU scheduling algorithms:

Note: 1 Second = 1000ms (milliseconds)

Time_to_Process = Wait_Time + Service_Time

System Oriented Statistics

CPU Utilization: % of time CPU is busy processing programs.

%Utilization = Arrival_Rate * Service_Time

In 1 avg. second 7 processes arrive, with service time = 100 ms each: Utilization = 7*.1 = 70%

In real world, it should range from 40% to 90%.

Throughput: The number of processes that are completed per time unit.

Assume processing times: Process 1: 300 ms; Process 2: 400ms; Process 3: 300ms.

Throughput = 3 processes in 1 second.

Wait Time: Sum of periods spent waiting in the ready queue.

Wait Time = EndTime – ArrivalTime – ServiceTime

User Oriented Statistics

Turnaround Time: The interval from time of submission to time of completion.

Used also with batch programs.

Includes non-CPU times: waiting to get into memory, waiting in ready queue, doing I/O.

TurnaroundTime = EndTime – ArrivalTime

Response Time: The interval from submission of a request until first response is produced.

Used with interactive programs.

Does not include time it takes to output the response (to the output device).

2 Seconds or less desirable.

Other concerns:

Predictability: Response time does not vary widely.

Optimize average, but guarantee all users get good service.

Scheduling Algorithms

First Come First Serve  = FCFS or FIFO

FCFS:  Processes that request the CPU first are allocated the CPU first.

Implemented with a FIFO queue of PCBs.

Nonpreemptive

Process	Arrive Time		Burst Time

P1			0			24

P2			0			3

P3			0			3

P1                               P2     P3

|------------------------------------------------|------|------|

0                                                          24    27     30

Average wait time: (0+24+27)/3 = 17 ms

Average turnaround time: (24+27+30)/3 = 81/3 = 27 ms

What happens if the processes arrive in order P2, P3, P1?  How does that impact Wait, Turnaround time?

Conclusion:

CPU-bound processes may get and hold (hog) the CPU.

Varied and poor response for I/O-bound processes.

Poor use of I/O devices.

Shortest Job First

Shortest Job First: CPU is assigned to the process that has the smallest expected CPU burst.

Examines the length of the next CPU-burst, not the total process length.

Nonpreemptive

Used in long-term scheduling

Problem: Must know length of next CPU request.

Process	Arrive Time		Burst Time

P1			0			6

P2			0			8

P3			0			7

P4			0			3

P4        P1            P3               P2

|------|------------|--------------|----------------|

0      3              9                16                 24

Average wait time: (0+3+9+16)/4 = 7ms.

Average turnaround time: (3+9+16+24)/4 = 13ms.

Conclusion:

Problems:

Starvation: Longer processes may never get time.

No preemption: Short processes must wait for a CPU-bound process.

How to predict length:

Batch: Use process time limit requested when submitting job.

Interactive: Take running average of burst length and use as predictor.

How to calculate running average length?

S(n+1) = pt(n) + (1-p)S(n)

where S(n) = running average at time n

t(n) = burst length at time n

p = weight factor, where 0 < p < 1

When p = 1/2 recent history and past history are equally weighted.

Larger p results in more weight on recent time intervals.

Given p = 0.5

S(n+1)	t(n)		S(n)

8		6		10

6		4		8

6		6		6

5		4		6

Shortest Remaining Time First

Shortest-Remaining-Time-First: Preempts current process if another process would complete sooner.

Always selects the process which will complete the soonest (like Shortest-Process-First)

Preemptive.

Process	Arrive Time		Burst Time

P1			0			8

P2			1			4

P3			2			9

P4			3			5

P1  P2        P4           P1                P3

|--|--------|----------|--------------|------------------|

0 1         5           10              17                    26

Average wait time: ((10-1) + (1-1) + (17-2) + (5-3)) / 4 = 26/4 = 6.5ms

Average turnaround time: (17 + (5-1) + (10-3) + (26-2)) / 4 = 13ms

Conclusion:

Advantage: A short job is given immediate preference to a running longer job.

Priority Scheduling

Priority Scheduling: High priority processes scheduled before low priority processes.

A priority is associated with each process.

Priority defined by: (E.g.) Foreground, Background, Real Time, Nice

Preemptive

Priorities can be defined:

Number of priorities may range.  Assume 0-1024:

High priority may be priority 0 or 1024, depending on system.

External or Internal Priorities:  Is priority determined external or internal to the O.S?

External:  Importance of process, $ paid for computer use, department priority.

Internal: Time limits, ratio of average I/O burst to average CPU burst, Aging.

Assume lower number is higher priority:

Process	Arrive Time		Burst Time		Priority

P1			0			10		3

P2			0			1		1

P3			1			2		3

P4			1			1		4

P5			1			5		2

P2             P5                                   P1                        P3     P4

|----|--------------------|----------------------------------------|--------|----|

0    1                       6                                                 16       18  19

Wait Times:

Priority 1: 0ms

Priority 2: 0ms

Priority 3: (6 + (16-1)) / 2 = 10.5ms

Priority 4: 18-1 = 17ms

How does the above change if P6 arrives at time 8 with a priority of 1 and a burst time of 3?

Conclusion:

Problems: Starvation or indefinite blocking.

Solution: Internal Priority

Aging: Raise priority for processes that have waited for a long time.

Example: Raise priority by one when process has waited 1 minute.

Eventually even lowest priority process becomes the highest priority process.

Round Robin

Round Robin: Every process gets a turn = one time quantum at CPU.

Timer interrupt causes scheduler to context switch.

Time quantum = time slice: 10-100ms long.

Preemptive

Ready queue is circular queue.

Assume time quantum is 4 ms long.

Process	Arrive Time		Burst Time

P1			0			24

P2			0			3

P3			0			6

P1     P2    P3     P1    P3     P1    P1     P1        P1

|--------|------|------|--------|------|-------|--------|--------|--------|

0        4       7      11       15      17       21       25       29       33

Average Wait Time: (4+9+11)/3 = 8 ms

Conclusion: Performance depends heavily on size of time quantum.

Optimum: 80% of CPU bursts should be < time quantum.

Optimum: Time quantum should be large with respect to context switch time.

If context switch is approx. 10% of time quantum, then about 10% of CPU time is spent in context switch.

Advantage: Performs reasonably well with short-term jobs.

Disadvantage: Additional overhead required due to additional context switching.

Disadvantage: I/O bound processes rarely use entire timeslice before blocking due to I/O.

Favors CPU-bound processes somewhat.

Multi-level Feedback Queue

Multilevel Feedback Queue:  Processes hogging CPU sink to lower priority levels.

- All processes start at Request Queue 0 (highest priority).

- When timeslice completed put in Request Queue 1.

- When timeslice completed put in Request Queue 2.

- When timeslice completed put in RQ ...

OS Implementation:

Operates strictly on priority:

Schedules processes in RQ 0 until it is empty, then processes RQ1...

All queues processed in FCFS order, except lowest priority queue that operates in RR.

Lower priority queues may get increasing time quantums.

Problem: Low priority queues may starve

Solution: Allow processes that have waited a certain length of time to rise back up the priority queues.

Assume RQ0 time quantum = 4, and RQ doubles the time quantum.

Process	Arrive Time		Burst Time

P1			0			24

P2			0			3

P3			6			3

P4			6			8

P1     P2     P3      P4          P1            P4                P1

|--------|------|------|--------|----------------|--------|------------------------|

0         4      7     10       14                 22       26                        38

Conclusion:

Advantage: General CPU scheduling solution

Disadvantage: Complex

##### Multiprocessing

Symmetric MultiProcessing (SMP):  Each processor runs an OS scheduler.

Asymmetric MultiProcessing:  One processor runs the scheduler and assigns jobs to the other processors

Load Balancing: Attempts to equalize the load between all processors.

This can be accomplished by migrating processes between processors.

Problem:  A process can already be in cache and repopulating the new cache may take time.

Solution:  Processor Affinity:  Assign a process to the processor where its cache is already loaded

##### Real Systems

Linux

Three scheduling classes:

- FIFO: FIFO real-time threads (preemptive by priority)

- RR: Round-robin real-time threads (preemptive by timeslice, scheduled by priority)

- Other: Non-real time threads (run if no real-time threads)

  - Non-real-time: priorities 100-139, default 120

  - Active queue list and expired queue list

Scheduling Algorithm:

Round-Robin within Priority: Time slices range between 10-200 ms, higher priority -> larger time slices

- Priority altered to favor I/O-bound tasks over CPU-bound tasks; high-sleep rate I/O bound highest priority.

Windows

Fully preemptive: Higher-numbered priority process preempts lower priority process

32 Ready Queues

16-31: Real-time queues: Priority is fixed

1-15: Variable level queues: For normal applications

Priority is lowered if timeslice completes or is a background window.

Priority is raised if I/O completes (keyboard raised lots, disk some)

0: Memory management

Idle Thread: Spare time or idle time task runs when nothing else runs

Java Thread Scheduling

JVM uses Priority-based scheduling, but may or may not be Preemptive

May or may not use timeslicing (not checked recently)

If timeslicing not used, a thread may yield control using Thread.yield()

Priorities range from 1 to 10, where 1 is low and 10 is high.

Priority can be changed using setPriority() method.

The JVM never alters the priority of a thread.

Algorithm Evaluation

Deterministic Modeling: Use a fixed scenario of processes/threads arriving, as in scheduling algorithm examples above.

Queuing Models: Uses mathematical (probabilistic) models to analyze given arrival rates, service times, (and potentially number of processors) to derive average wait time and turnaround time.

Simulation: Randomly generates job arrivals with random service times, and simulates the processing of these random jobs over a sufficiently long duration of time to generate average wait time and turnaround times.

Queuing Statistics

Inter-arrival Time:  The average timer between incoming requests

Arrival Rate:  1/InterArrivalTime = The number of requests that arrive on average in a specified time unit

Service Time:  The average time it takes to service a request

Service Rate:  1/ServiceTime = The number of requests that can be handled in a specified time unit.

Offered Rate: ArrivalRate/ServiceRate = ServiceTime/InterArrivalTime = The average number of requests being handled in a system, if no requests are discarded.

## Exercise

Assume the following conditions (where low numbers are higher priority).  For each method, draw a timeline and complete the per-job and total Wait Time and Turnaround Time.

Shortest Job First (No Preemption)

| Job # | Arrival Time | Service Time | Turnaround Time | Wait Time |
| --- | --- | --- | --- | --- |
| 1 | 0 | 2 |  |  |
| 2 | 0 | 4 |  |  |
| 3 | 3 | 1 |  |  |
| 4 | 5 | 8 |  |  |
| 5 | 6 | 3 |  |  |
| 6 | 11 | 3 |  |  |
| Total /Avg |  |  |  |  |

Shortest Remaining Time First (Preemption)

| Job # | Arrival Time | Service Time | Turnaround Time | Wait Time |
| --- | --- | --- | --- | --- |
| 1 | 0 | 2 |  |  |
| 2 | 0 | 4 |  |  |
| 3 | 3 | 1 |  |  |
| 4 | 5 | 8 |  |  |
| 5 | 6 | 3 |  |  |
| 6 | 11 | 3 |  |  |
| Total /Avg |  |  |  |  |

Priority (Preemptive) Lower numbers = higher priority.

| Job # | Arrival Time | Priority | Service Time | Turnaround Time | Wait Time |
| --- | --- | --- | --- | --- | --- |
| 1 | 0 | 10 | 2 |  |  |
| 2 | 0 | 10 | 4 |  |  |
| 3 | 3 | 3 | 1 |  |  |
| 4 | 5 | 10 | 8 |  |  |
| 5 | 6 | 3 | 3 |  |  |
| 6 | 11 | 10 | 3 |  |  |
| Total /Avg |  |  |  |  |  |

Round Robin (Timeslice = 3 ms)

| Job # | Arrival Time | Service Time | Turnaround Time | Wait Time |
| --- | --- | --- | --- | --- |
| 1 | 0 | 2 |  |  |
| 2 | 0 | 4 |  |  |
| 3 | 3 | 1 |  |  |
| 4 | 5 | 8 |  |  |
| 5 | 6 | 3 |  |  |
| 6 | 11 | 3 |  |  |
| Total /Avg |  |  |  |  |